## Slide 1: Smart Fire Safety System
Priyam Das
Gourav Dey
Manoj
Pritam Pramanik
Aishik Paul

## Slide 2: A smart fire safety system designed to autonomously detect and extinguish fires, delivering real-time information to users and seamlessly executing advanced tasks necessary in emergency situations.
Introduction

## Slide 3: The Problem Statement

## Slide 4: The Geneva Association estimates the annual cost of fire losses at approximately 1% of global GDP based on data from various countries. Global insured fire losses at $37 billion in 2021- The Munich Re report "Natural disaster risks - Rising trend in losses“ As per the National Crime Records Bureau, between 2001 to 2014, about over 60 people die every day and about 25,000 persons die every year due to fires and related causes, in India. A total of 3.16 lakh fire accident cases were reported in the country. Fire incidents killed 35 people daily between 2016 and 2020, as per NCRB. About Rs. 1000 crores are lost every year due to fire in India. A 2018 study published in Fire Technology found that every minute delay in firefighter arrival increased property damage by 1.04%.
Surveys and Reports

## Slide 5: Impacts and Origins of Fire Hazards
Human Toll:
Loss of life and severe injuries
Property and Infrastructure Destruction:
Damage to buildings, homes, public spaces and massive property loss
Electrical Challenges:
Faulty wiring and electrical malfunctions.
Human Factors:
Human error, accidents and misuse of flammable materials.
Appliance and Equipment Risks:
Defective appliances and improper use.

## Slide 6: Mitigating Fire Hazards
Early Detection Systems:
Implementing advanced technologies for early identification of potential fire risks.
Smart Fire Safety Devices:
Introducing intelligent devices, to autonomously suppress fires without human intervention.
Emergency Planning using AI:
Developing AI infused technologies for response and evacuation during emergency
Employee Training and Awareness:
Conducting training programs to educate individuals on fire safety measures
Strict Adherence to Safety Standards:
Ensuring compliance with industry safety standards and regulations.

## Slide 7: Solution

## Slide 8: Solution Overview
Autonomous Fire Detection and Extinguishing:
Automatic detection and suppression of fires
Real-time User Notifications:
Real-time notifications in case of critical situations conveying details to users
Automated Emergency Response:
Automatic calls to rescue teams and providing estimated time of arrival (ETA)
Evacuation Route Planning:
Evacuation routes using building or infrastructure blueprint
Continuous Monitoring and Updates:
Continuous monitoring and updates at regular time intervals

## Slide 9: Technical Stack
Sensor Integration:
advanced sensors, including smoke detectors, heat sensors and computer vision
Actuation Systems:
responsive actuation systems for swift and targeted fire suppression, using agents such as water, foam, or gas.
IoT Communication:
Internet of Things (IoT) communication for real-time data transmission and seamless interaction
Machine Learning Algorithms:
machine learning algorithms for intelligent decision-making, enhancing the system's ability to adapt to diverse fire scenarios.

## Slide 10
BLOCK DIAGRAM
ARDUINO
System to be implemented in the Robot
System to be implemented in WebApp
SENSORS
Flame Sensor Module
MQ-2 Smoke Sensor
Thermal Imaging Camera (IR Imaging Camera)
(AMG8833)
LOCATION
GPS Module (GPS Neo-6M)
COMMUNICATION
Wi-Fi Module (ESP 32)
WebApp
Generate ALARM or TEXT MESSAGE
Instant ALARM Generation
Location of Fire
Intensity of Fire
Automated Response
Evacuation Route through app
Contact rescue team
Continuous monitoring and updates.

## Slide 11
PROCESS FLOWCHART
ARDUINO
*working is mentioned in the algorithm
Wi-Fi Module
GPS Module
(GPS Neo-6M)
Flame Sensor
Smoke Sensor
Thermal (IR) Imaging(AMD8833)
Location of the Robot
Fire Source detection
(Location of Fire)
If FIRE is Detected
If FIRE is Detected
Data sent to WebApp
Flame Sensor
Smoke Sensor
Thermal (IR) Image
GPS Module
Drive the Robot to the Location of Fire
Turn on Water Pump in Water Tank
and
Sprinkle Water to Extinguish Fire

## Slide 12: Algorithm
Step 1: ff = front flame sensor value; frf = front-right flame sensor value; flf = front-left flame sensor value
rf = right flame sensor value; lf = left flame sensor value
bf = back flame sensor value; brf = back-right flame sensor value; blf = back-left flame sensor value
Step 2: fmax = max(ff, frf, flf, rf, lf, bf, brf, blf)
Step 3: if(fmax=ff)
go FRONT
turn ON all motors in FORWARD direction
Step 4: if(fmax=frf)
TURN 45 degrees right
turn ON left-front and left-back motors in FORWARD direction
if(fmax=ff)
STOP motors
turn ON all motors in FORWARD direction
Step 5: if(fmax=flf)
TURN 45 degrees left
turn ON right-front and right-back motors in FORWARD direction
if(fmax=ff)
STOP motors
turn ON all motors in FORWARD direction
Step 6: if(fmax=rf)
TURN 90 degrees right
turn ON left-front and left-back motors in FORWARD direction
if(fmax=ff)
STOP motors
turn ON all motors in FORWARD direction
Step 7: if(fmax=lf)
TURN 90 degrees left
turn ON right-front and right-back motors in FORWARD direction
if(fmax=ff)
STOP motors
turn ON all motors in FORWARD direction
Step 8: if(fmax=bf)
go BACK
turn ON all motors in BACKWARD direction
Step 9: if(fmax=brf)
TURN 45 degrees right in BACKWARD direction
turn ON left-front and left-back motors in BACKWARD direction
if(fmax=bf)
STOP motors
turn ON all motors in BACKWARD direction
Step 10: if(fmax=blf)
TURN 45 degrees left in BACKWARD direction
turn ON left-front and left-back motors in BACKWARD direction
if(fmax=bf)
STOP motors
turn ON all motors in BACKWARD direction
Step 11: if(fmax>=fmax(thresh))
STOP all motors
START water pump and SERVO: Sprinkle water
if(fmax<=fmax(thresh1))
STOP water pump and SERVO
Fire
Extinguisher
Robot Vehicle
front flame sensor
right flame sensor
left flame sensor
front-right flame sensor
Front-left flame sensor
back-left flame sensor
back flame sensor
back-right flame sensor
Right-Front Motor
Right-back Motor
left-Front Motor
Right-back Motor
Water Tank with Pump
Water pipe from Water tank with Servo
Water pipe from Water tank with Servo
Structure of the Fire Extinguisher Robot Vehicle
Arduino
Motor Driver
*Wire connections are not shown in the schematic diagram

## Slide 13
Key Challenges:
Designing robust sensors for reliable fire detection in diverse conditions, including smoke, heat, and flame detection.
Engineering mobility systems to navigate through different terrains and obstacles effectively, including stairs and uneven surfaces.
Integrating efficient fire suppression mechanisms, such as water tanks, foam sprayers, or CO2 extinguishers, while considering weight, volume, and refillability.
Implementing advanced navigation and mapping algorithms to enable the robot to locate fires accurately and plan efficient routes.
Ensuring the robot's autonomous operation is safe and reliable, with features to prevent accidents and mitigate risks to humans and property.
Addressing potential limitations, such as battery life, operating temperature ranges, and environmental factors that may affect performance.

## Slide 14
Target Environments:
Industrial facilities, warehouses, and manufacturing plants.
High-rise buildings, including offices and residential complexes.
Hazardous environments, such as chemical plants or oil refineries.
Desired Outcomes:
Development of a prototype fire extinguisher robot capable of autonomously detecting and extinguishing fires in controlled testing environments.
Validation of the robot's effectiveness in reducing response times and minimizing human intervention during firefighting operations.
Demonstration of the robot's scalability and adaptability for deployment in real-world scenarios, potentially saving lives and mitigating property damage.

## Slide 15: Equipments
Arduino UNO
IR sensors
Servo
Motors
Motor Driver IC
Water Pump
Bread Board
Jumper Wires
Water Tank

## Slide 16: Future Scope

## Slide 17: Conclusion
Promising solution to enhance fire safety in various environments.
Addressing key challenges in sensor technology, mobility, fire suppression mechanisms, and autonomous operation: Potential to significantly reduce response times and minimize risks to both humans and property.
With further refinement and validation, fire extinguisher robots can play a crucial role in firefighting efforts, ultimately saving lives and mitigating the impact of fires on communities and ecosystems.